## Slide 1
Neuroergonomic Assessment of
Human Robot Interaction
Dominik Limbach, B.Sc.
24.01.2020
1
Kolloquium – Master Thesis
Systems Neuroscience & Neurotechnology Unit
Saarland University of Applied Sciences
Faculty of Engineering

## Slide 2: Outline
Dominik Limbach, B.Sc.
24.01.2020
2
Introduction
Problem Analysis & Goals
Materials & Methods
Results
Conclusion & Future Work

## Slide 3: Introduction
Dominik Limbach, B.Sc.
24.01.2020
3
Neuroergonomics
The study of brain and behaviour at work. (Parasuraman, 2003)
Comprised of neuroscience and ergonomics
Investigation of the neural bases of perceptual and cognitive functions, as well as, physical performance in relation to technologies and real world settings
Utilization of physiological measures that, directly or indirectly, reflect aspects of brain function.
Notes: The most direct measures are derived from the brain itself
E.g. Electroencephalogram (EEG), Event-Related Potentials (ERPs), Positron Emission Tomography (PET) and functional Magnetic Resonance Imaging (fMRI)

## Slide 4: Introduction
Dominik Limbach, B.Sc.
24.01.2020
4
Applications of Neuroergonomics
Understanding of how the brain carries out complex tasks of everyday life
To design technologies and work environments for safer and more efficient operation
To advance the understanding of brain function in relation to human performance in real-world tasks
Notes: But Why do we need Neuroergonomics?
Well, if we are able to understand … line 1
We can use this knowledge to… point 1, point 2

## Slide 5: Introduction
Dominik Limbach, B.Sc.
24.01.2020
5
Automated Workplaces
Optimizing Human Machine Interaction
Concept of adaptive automation, work environment sensitive to the mental state of the operator
Increase system performance and safety by reducing stress and human error, induced by static automation
Regulatory approach: Task allocation based on continuous monitoring of the human operator in conjunction with emotion recognition
Notes: An recent example is HRI
In particular, Adaptive Automation Workplaces
Where some tasks are automated and humans need to interact with machines

## Slide 6: Problem Analysis
Dominik Limbach, B.Sc.
24.01.2020
6
Research on the matter, based on
Non representative subject groups (i.e. children, or a single subject)
Unauthentic data (selection bias, ideal recording conditions)
Obtrusive and expensive measurement methods (fMRI, PET, EEG)

## Slide 7: Goals
Dominik Limbach, B.Sc.
24.01.2020
7
The facilitation of signal based emotion recognition in Human Robot Interaction by providing an unobtrusive monitoring method for peripheral physiological signals

## Slide 8: Scope
Dominik Limbach, B.Sc.
24.01.2020
8
Design and Implementation of a wireless measurement system capable of real-time data acquisition, based on a wrist-worn device
Build a database for machine learning
Evaluate system capabilities based on the classification accuracy of selected machine learning algorithms

## Slide 9: Materials & Methods
Dominik Limbach, B.Sc.
24.01.2020
9
Empatica E4 Wristband
A medical grade wearable for real-time data acquisition
Capable of wireless data transmission
Designed for daily life usage

## Slide 10: Materials & Methods
Dominik Limbach, B.Sc.
24.01.2020
10
Physiological Channels
Blood Volume Pulse (BVP)
Galvanic Skin Response (GSR)
Skin Temperature (ST)

## Slide 11: Materials & Methods
Dominik Limbach, B.Sc.
24.01.2020
11
Data Collection Experiment
14 participants, 7 male/ 7 female, aged 24-50 years
Mental Arithmetic Stress Test (Jern et al., 1991), Stroop Test
Visual Stimulation (IAPS, Lang et al., 2008)
Notes: 2 cognitive tasks to induce stress by presenting different levels of workload
Stroop test: naming colors used to write an incongruous color name. task requires subjects to override a reading response. This conflict interference
situation is called the Stroop Effect
Visual stimulation for emotion elicitation

## Slide 12: Materials & Methods
Dominik Limbach, B.Sc.
24.01.2020
12
Experimental Procedure
Baseline Measurement
Mental Arithmetic Stress Test
Stroop Test
Visual Stimulation (Set 1, 32 p., pleasant)
Visual Stimulation (Set 2, 30 p., unpleasant)
5 min per session
Cooldown session after each task

## Slide 13: Materials & Methods
Dominik Limbach, B.Sc.
24.01.2020
13
Experimental Setup
Notes: Due to the unobtrusive nature of our recording device the setup was minimalistic

## Slide 14: Materials & Methods
Dominik Limbach, B.Sc.
24.01.2020
14
Selected Algorithms
Choosen from the top 10 algorithms in data mining. (Wu et al., 2008)
K - Nearest Neighbor Classifier (kNN)
Support Vector Machines (SVM)
Random Forest Classifier (RFC)
Neural Networks (NN)

## Slide 15: Materials & Methods
Dominik Limbach, B.Sc.
24.01.2020
15
Data Processing Steps
Notes: Data Extraction: Access raw signal data recorded with the E4
<- using Streaming server App, Bluetooth dongle and TCP Client (implemented in matlab)

## Slide 16: Signal Processing & Analysis
Dominik Limbach, B.Sc.
24.01.2020
16
Notes: Filtering for GSR/ST : zero phase fourth order Butterworth filter, cutoff 1.0Hz

## Slide 17: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
17
Zero-phase second-order Butterworth, bandpass of 0.5-8Hz
Notes: Elgendi et al 2013
Filtering, to remove the baseline wander and high frequencies that do not contribute to the
systolic peaks

## Slide 18: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
18
Notes: Clipping, keeping only the signal above 0

## Slide 19: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
19
Notes: Squaring, to emphasize large differences resulting from sytolic waves

## Slide 20: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
20
Generating event-related moving averages
  MA_peak: emphasizes the systolic peak area (W1 = 111ms)
  MA_beat: empasizes the beat area (W2 = 667ms)
Notes: Parameter optimization:
[Elgendi et al. 2013]
Performance evaluation based on Sensitivity (SE = TP/(TP+FN)) and Positive Predictivity +P= TP/(TP+FP)
Brute force search optimization for systolic peak detection function:
-Parameter: PPG signal, frequency Band (F1-F2), event-related duration (W1, W2) and offset (ß)

## Slide 21: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
21
Generating Blocks of Interest
  A new block was created for every interval where MA_peak exceeded a certain threshold THR1
Notes: Parameter optimization:
[Elgendi et al. 2013]
Performance evaluation based on Sensitivity (SE = TP/(TP+FN)) and Positive Predictivity +P= TP/(TP+FP)
Brute force search optimization for systolic peak detection function:
-Parameter: PPG signal, frequency Band (F1-F2), event-related duration (W1, W2) and offset (ß)

## Slide 22: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
22

## Slide 23: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
23
Select valid Blocks of Interest
  A block was marked as valid, if it was wider than THR2 = W1

## Slide 24: BVP Peak Detection
Dominik Limbach, B.Sc.
24.01.2020
24

## Slide 25: Editing Process
Dominik Limbach, B.Sc.
24.01.2020
25
Inter-Beat-Interval (IBI) were calculated, using the distance between successive peaks

## Slide 26: Editing Process
Dominik Limbach, B.Sc.
24.01.2020
26
Identifcation of outlier intervals (45 bpm > HR > 191 bpm)
All outlier sequences with a length greater than 3 seconds were considered artefacts and removed, the rest interpolated. (Clifford, 2002)

## Slide 27: Editing Process
Dominik Limbach, B.Sc.
24.01.2020
27
Identifcation of ectopic beats using Kamath‘s rule. (Choi et al., 2016)
An interval was considered abnormal, if it increased by more than 32.5% or decreased by more than 24.5% compared to the previous interval

## Slide 28: Editing Process
Dominik Limbach, B.Sc.
24.01.2020
28
All intervals that were marked as abnormal were replaced using linear interpolation of the surrounding intervals
The number of inserted intervals B was calculated according to the total time encompassed by the ectopic beat/ or sequence. (Lippman et al., 1994)

## Slide 29: Editing Process
Dominik Limbach, B.Sc.
24.01.2020
29
Data was considered valid if at least 80% of a 5 minute segment consisted of acceptable IBIs. (Clifford, 2002)

## Slide 30: Editing Process
Dominik Limbach, B.Sc.
24.01.2020
30
Heart rate variability (HRV), i.e. variations in the length of consecutive heart beat intervals
HRV feature extraction and selection according to the guidelines provided by the Task Force of The European Society of Cardiology and The North American Society of Pacing and Electrophysiology (1996)

## Slide 31: Feature Selection
Dominik Limbach, B.Sc.
24.01.2020
31
HRV Measures – Time Domain

## Slide 32: Feature Selection
Dominik Limbach, B.Sc.
24.01.2020
32
HRV Measures – Frequency Domain
Notes: Power represented by average bandpower in the respective frequency band.
Average Bandpower calculated using Welch‘s method (Hann window): Calculates estimate of the spectral density by dividing the data into overlapping segments, computing a modified periodogram of each segment, and averaging all periodograms. Bandpower is then calculated by integrating over the frequency bands.(trapezoidal rule)
Preparation: Discrete event series (ibi tachogram interpolated with a frequency of 7 Hz)
Power spectral density (PSD) analysis provides the basic information of how power (i.e. variance) distributes as a function of frequency. Independent of the method
employed, only an estimate of the true PSD of the signals can be obtained by proper mathematical algorithms. (Task Force)
Variance, is the expectation of the squared deviation of a random variable from its mean. (IBI [ms] -> Variance [ms**2]

## Slide 33: Feature Selection
Dominik Limbach, B.Sc.
24.01.2020
33
GSR
ST

## Slide 34: Data Interpretation
Dominik Limbach, B.Sc.
24.01.2020
34
Data Preparation
Generating Data- and Feature Sets
Split Data sets into training and test samples
Feature Normalization for SVM, NN
Notes: Prior to algorithm training we prepared the data

## Slide 35: Data Interpretation
Dominik Limbach, B.Sc.
24.01.2020
35
Data Sets
Complete set, featuring data of all recording sessions and a total of 6 session types
Subsets to evaluate the performance on binary classification tasks, aiming to
Identify individual emotional states
Distinguish between similar emotional states

## Slide 36: Data Interpretation
Dominik Limbach, B.Sc.
24.01.2020
36
Feature Sets
To investigate the effects of certain feature combinations and individual feature groups
Complete, 21 features (HRV, GSR, ST)
Reduced T, 14 features, (HRV time, GSR, ST)
Reduced F, 13 features, (HRV frequency, GSR, ST)
Single Sets
Notes: Investigate the effects of certain feature combinations and individual feature groups

## Slide 37: Data Interpretation
Dominik Limbach, B.Sc.
24.01.2020
37
Hyperparameter Optimization – Grid Search
Hyperparameters, are algorithm specific parameters that control the learning process and are set beforehand (e.g. the hidden layer size or the learning rate of a Neural Network)
Choosing an optimal set of hyperparameters, by exhaustively searching through a specified subset of the hyperparameter space of a learning algorithm
3-, 5-fold Crossvalidation to improve generalization
for all four algorithms and all possible combinations of feature- and data sets
Notes: k-Fold Cross-Validation
Cross-validation is a resampling procedure used to evaluate machine learning models on a limited data sample.
The general procedure is as follows:
Shuffle the dataset randomly.
Split the dataset into k groups
For each unique group:
  Take the group as a hold out or test data set
  Take the remaining groups as a training data set
  Fit a model on the training set and evaluate it on the test set
  Retain the evaluation score and discard the model
Summarize the skill of the model using the sample of model evaluation scores
Importantly, each observation in the data sample is assigned to an individual group and stays in that group for the duration of the procedure. This means that each sample is given the opportunity to be used in the hold out set 1 time and used to train the model k-1 times.

## Slide 38: Data Interpretation
Dominik Limbach, B.Sc.
24.01.2020
38
Evaluation
Based on the classification accuracy of the best estimators (determined by Grid Search) on the reserved test data
Notes: k-Fold Cross-Validation
Cross-validation is a resampling procedure used to evaluate machine learning models on a limited data sample.
The general procedure is as follows:
Shuffle the dataset randomly.
Split the dataset into k groups
For each unique group:
  Take the group as a hold out or test data set
  Take the remaining groups as a training data set
  Fit a model on the training set and evaluate it on the test set
  Retain the evaluation score and discard the model
Summarize the skill of the model using the sample of model evaluation scores
Importantly, each observation in the data sample is assigned to an individual group and stays in that group for the duration of the procedure. This means that each sample is given the opportunity to be used in the hold out set 1 time and used to train the model k-1 times.

## Slide 39: Results
Dominik Limbach, B.Sc.
24.01.2020
39

## Slide 40: Results
Dominik Limbach, B.Sc.
24.01.2020
40

## Slide 41: Conclusion & Future Work
Dominik Limbach, B.Sc.
24.01.2020
41
Conclusion
Realization of real-time data acquisition using the Empatica E4
Established a database for machine learning, deploying our wireless recording system in an experimental setting
Providing a method for coarse emotion classification using peripheral physiological signals, i.e. individual emotional states
Further optimization is needed to increase capability in more complex classification tasks

## Slide 42: Conclusion & Future Work
Dominik Limbach, B.Sc.
24.01.2020
42
Future Work
Large Scale Data Collection
Artefact Compensation, for motion based artefacts introduced by sensor displacement or muscle activity
HRI Focused Experiment, authentic data collection and emotion elicition

## Slide 43: References
Dominik Limbach, B.Sc.
24.01.2020
43
R. Parasuraman. Neuroergonomics: Research And Practice. Theoretical Issues in Ergonomics Science, 2003.
Task Force of The European Society of Cardiology and The North American Society of Pacing and Electrophysiology. Heart rate variability. Standards of measurement, physiological interpretation, and clinical use. European Heart Journal, 1996.
X. Wu, V. Kumar, J. R. Quinlan, J. Gosh, Q. Yang, H. Motoda, G. J. McLachlan, A. Ng, B. Liu, P. S. Yu, Z.-H. Zhou, M. Steinbach, D. J. Hand, and D. Steinberg. Top 10 Algorithms In Data Mining. Knowl Inf Syst, 2008.
E. A. Byrne and R. Parasuraman. Psychophyiology And Adaptive Automation. Biological Psychology, 1996.
A. Choi and H. Shin. Quantative Analysis of the Effect of an Extopic Beat on the Heart Rate Variability in the Resting Condition. Frontiers in Physiology, 2016.
G. D. Clifford. Signal Processing Methods for Heart Rate Variability. PhD thesis, St. Cross College, 2002.
M. Elgendi, I. Norton, M. Brearley, D. Abbott, and D. Schuurmans. Systolic Peak Detection in Acceleration Photoplethysmograms Measured from Emergency Responders in Tropical Conditions. PLoS ONE, 2013.

## Slide 44: References
Dominik Limbach, B.Sc.
24.01.2020
44
P. J. Lang, M. M. Bradley, and B. N. Cuthbert. International Affective Picture System (iaps): Affective Ratings Of Pictures And Instruction Manual. Technical Report A-8, University of Florida, Gainesville, FL., 2008.
N. Lippman, K. M. Stein, and B. B. Lerman. Comparison Of Methods For Removal Of Extopy In Measurement Of Heart Rate Variablility. American Journal of Physiology, 1994.
Empatica, Via Stendhal 36, 20144 Milano (MI). E4 Wristband From Empatica. User’s Manual.
M. Mitrushina, K. B. Boone, J. Razani, and L. F. D’Elia. Handbook of Normative Data for Neuropsychological Assessment. Oxford University Press, USA, 2005.

## Slide 45
Dominik Limbach, B.Sc.
24.01.2020
45
Thank you very much for your attention !